## Slide 1: Basic Stamp Quick Start

## Slide 2: Basic Stamp II
Self contained computer
  “Micro-controller”
    Specialized for “embedded” computing (sensing and controlling things)
  Built in programming language
    PicBasic (interpreted)
    Small programming environment runs on a PC
      Connected with a serial cable

## Slide 3: Parallax Basic Stamp II
PIC processor
  (Very) roughly the computing power on the lunar module (much faster, but much less memory)
  1 million instructions / sec
Non-volatile memory
Power regulation
Serial interface
{
}

## Slide 4: Parallax Basic Stamp II
Input/output pins
  16 total (P0…P15)
  This is where the action is
  Each pin can be accept input or produce output
    Logic levels (0 or +5v)
    Also “tricks” for sensing and producing values in between

## Slide 5: Getting Started
Download the documentation
  The Basic Stamp Manual v2.0 (2.0MB)
http://parallaxinc.com/downloads/Documentation/Basic%20Stamps/BASIC%20Stamp%20Manual%20v2.0.pdf
    351 pages (probably worth printing [2up, double sided])
  Basic Stamp I Application Notes
http://parallaxinc.com/downloads/Documentation/Basic%20Stamps/BASIC%20Stamp%201%20App%20Notes%20v1.9.pdf
  Basic Stamp II Application Notes
http://parallaxinc.com/downloads/Documentation/Basic%20Stamps/BASIC%20Stamp%202%20App%20Notes%20v1.9.pdf
Download the programming environment
http://parallaxinc.com/downloads/software/BASIC_Stamps/Setup%20Stamp%20Editor.exe

## Slide 6: Documentation
Manual Covers all types of Basic Stamps
  BS1 older, smaller, slower, lesser lang, cheaper
  BS2 what we are using, 26 bytes for vars
  BS2e 8x instruction memory, more pin current +64 bytes RAM, a few extra features
  BS2sx 2.5x faster than BS2
  BS2p 24 3x faster than BS2, +128 bytes RAM many new language & I/O features
  BS2p 40 BS2p with 32 I/O pins

## Slide 7: Documentation
Manual
  Covers basic setup
    Power and serial connections
  Mostly a language reference manual
    Very simple (“krufty” / dumb) language
    Think of it as a glue to hold together a nice I/O subroutine library
Applications Manual
  Examples are here
  Most are in BS1 (have to adapt code and pins)

## Slide 8: Let’s Build Stuff…
Solderless breadboard
  Component pins / leads or wires push into the wholes
  All main rows connected together
  Four vertical buses also connected
Push the BS2 in at top
  Rows 1…12 across gap
  Pin 1 to the top-left
  Note simulated notch

## Slide 9: Pins on the BS2 package
(1) SOUT
(2) SIN
(3) ATN
  Serial connection to PC
  To DB9 pins 2,3,4
(4) Vss
  Ground
  Pin 5 on DB9
Also connect DB9 pin 6 to DB9 pin 7

## Slide 10: Pins on the BS2 package
(1) Sout
(2) Sin
(3) ATN
  Serial connection to PC
  To DB9 pins 2,3,4
(4) Vss
  Ground
  Pin 5 on DB9
Also connect DB9 pin 6 to DB9 pin 7

## Slide 11: Pins on the BS2 package
(24) Vin
  Power in
  5.5-15v unregulated
  Red wire of 9v battery
(23) Vss (same as pin 4)
  Ground (black wire of 9v)
  Connect to blue bus
(22) Vdd
  +5v out (regulated)
  Connect to red bus

## Slide 12: Pins on the BS2 package
(5…12) I/O pins
  P0…P7
  Each has 20mA out limit
  Each has 25mA in limit
  50mA max total
(13…20) I/O pins
  P8…P15
  Same current limits

## Slide 13: Connect and try it…
Run programming environment
Type in this program:
    debug “Hello world!”, cr
    end
Save your program! (ctrl-S)
  Environment will hang on occasion
Run it
  Type ctrl-R, press “play” icon, or choose from “Run” menu

## Slide 14: Hardware Hello World
Pop quiz:
  We want to drive this LED at about 10mA
  What’s the value of the resistor?
P0

## Slide 15: Hardware Hello World
500Ω (but only had 470Ω…)
Wire this…
  Long wire on LED is positive side
Program
      out_pin con 0
      top:
      high out_pin
      pause 500
      low out_pin
      pause 500
      goto top
P0

## Slide 16: About the Program
out_pin con 0 ’const declaration
top: ’label
high out_pin ’pull pin high (+5v)
pause 500 ’delay 500ms
low out_pin ’pull pin low (0v)
pause 500 ’delay 500ms
goto top ’do it again

## Slide 17: Push Button Input
What’s the difference?

## Slide 18: Push Button Input
What’s the difference?
  Active high (right) vs. active low (left)
Why 10K?

## Slide 19: Push Button Input
What’s the difference?
  Active high (right) vs. active low (left)
Why 10K?
  Not critical,but don’t need much current
.

## Slide 20: Push Button Input
What’s the difference?
  Active high (right) vs. active low (left)
Why 10K?
  Not critical,but don’t need much current
We’ll use this one

## Slide 21: Push Button Input
Program
  led var out0 ' declare out to be same as pin 0
  sw var in1 ' declare in to be same as pin 1
  cnt var byte ' counter var
  input sw ' init pin directions and values
  output led : low led
  cnt=0
  loop:
  cnt = cnt + 1 ' count times through loop
  led = sw & cnt ' LED when sw & every other loop
  pause 100 ‘ leave LED on/off for a bit
  goto loop

## Slide 22: Sound output
FREQOUT Pin, Len, Freq1
FREQOUT Pin, Len, Freq1, Freq2
Len in ms
Freq in Hz
  0 for off

## Slide 23: Measuring Resistance
220Ω for current limiting if R goes to 0
  Most values in 100s ok
Different C’s and R’s will result in different time ranges
  See manual
  0.1 µF fine
rctime pin, 1, result
  Returns time in 2 µsec units

## Slide 24: How Does This Work?
Set pin to output and charge the capacitor
Flip pin to input and time how long until it drops below the minimum
  Time depends on C and R
    For fixed C, depends on R
  See manual for formula

## Slide 25: DC Motors
PWM: “Pulse Wave Modulation”
  Turns pin on a certain % of the time
  With proper filtering (or for slowly responding devices) gives you a good approximation to an analog output (0…5v)
PWM pin, duty, ms
  Duty: 255 = 100%

## Slide 26: Servo Motors
Servo motors turn to specific angle and hold
  ~0…180°
  Used for RC planes, etc.
Controlled based on pulses of a certain width (time)
  1ms  0°
  2ms  180°
  Delivered at least every 20ms (exact timing there not critical)

## Slide 27: Servo Motors
pulseout pin, time
  Delivers a pulse of given duration
  time in units of 2 µsec
Servos have 3 wires
  Power & Ground (to motor)
    Typically red and black (brown on ours)
  Control (to pin)
    Typically some other color
  Ordered: Ground, Power, Control on 3 pin connector

## Slide 28: Other Requested Sensors or Actuators?