## Slide 1: METC 143 Lab NOTEBOOK SPRING 2014
Tanner

## Slide 2: Instron 5960 Dual Column Table top Universal Testing System
By: “Wild” Billy and Tanner

## Slide 3: What it is.
We know it best as one of our tensile testers
Universal, static testing systems that perform tensile and compression testing
Can also perform shear, flexure, peel, tear, cyclic, and bend tests.

## Slide 4: Features
Load measurement accuracy: +/- 0.5%
Up to 2.5 kHz data acquisition rate
Speed range of 0.001 - 3000 mm/min
50 kN (11,250 lbs) capacity
1212 mm (47.7 in) vertical test space

## Slide 5: How it works
Pressure is applied from various directions, to test different properties of the metal.
  Compression
  Tension
  As well as a variety of other tests

## Slide 6: Instron in Action!!!!!
http://www.youtube.com/watch?v=ivTHHyHTjNU

## Slide 7: Source
http://www.instron.us/wa/product/5960-Dual-Column-Testing-Systems.aspx

## Slide 8: Lab 2/ Crystallography Lab
Post-Activity Questions
1. In this activity, you broke two silicon wafers. One wafer had a (100) crystal surface
plane orientation and the other a (111) surface plane orientation. In the making of the
original silicon ingot, what determined the crystal orientation of the silicon wafer? The number of surface atoms are
2. At what approximate angle did the (111) wafer b
break? It broke into 6 separate 60 degree pieces
3. At what approximate angle did the (100) wafer break? It broke into 4 separate 90 degrees pieces
4. Did each wafer continue to break at the same angle when you broke the smaller pieces?
Why or why not? Silicon wafer (100) broke an individual piece for second time the results were not exactly 4 90 degree pieces like before but for the most part rectangles or perfect squares. Silicon wafer (111) when a piece was broken for a second time, broke into 6 almost exact representational pieces of the original broken pieces as the first break was.
5. Which orientation (100) or (111) has more silicon atoms exposed to the wafer's surface? 111
6. Why is crystal orientation important in the fabrication of microsystems? To be able to know and produce a piece of material with the necessary requirements that particular piece of material needs to at hear to.
7. Identify the crystal orientation of each of the following pieces of silicon.

## Slide 9: Lab 2 Cont…..

## Slide 10: Lab 3 T9014 Aluminum

## Slide 11: Lab 3 Cont……

## Slide 12: Lab 4: TC1548 Steel Tensile Tester

## Slide 13: Lab 4: Cont….

## Slide 14: Lab 4: Cont…..

## Slide 15: Lab 4: Cont…

## Slide 16: Lab 5: Brinell & Rockwell Hardness Testing on Cu/Al

## Slide 17: Lab 5: Cont….

## Slide 18: Lab 5: Cont… Cu sample

## Slide 19: Lab 5: Cont…
Copper Trend Line
Froce
3000
kg
PI()
3.141593
Diameter
10
mm
d
6.98
mm
HB=
67.27172

## Slide 20: Lab 5: Cont…. Al sample

## Slide 21: Lab 5: Cont…
Al Trend line Curve

## Slide 22: Lab 6: Beginning of Pasco Strength Tester
Making our samples

## Slide 23: Lab 7: Rockwell Hardness Test of Al, Steel, & Brass