## Slide 1: Theorems and Proofs
EECT 112
Nathaniel Paulus
Fall 2017

## Slide 2: Methodology
Each of the simulations used for proof of the various theorems uses an indicator with a 2.5V threshold. In a real-world situation the 2.5V threshold may be problematic because it does not correspond to real threshold values. However, because everything in this simulation is about Boolean logic, the only values we are considering is 1 and 0. The 2.5V then can be ignored for most purposes.

## Slide 3: Theorem 1
Theorem 1: x∙0=0
Theorem 1 |  | 
x∙0=0 |  | 
x | y | 
0 | 0 | 0
1 | 0 | 0
Truth Table
Theorem 1.ms14
If any variable is ANDed with 0, the result must be 0.
The theorem is proven by simulation.

## Slide 4: Theorem 2
Theorem 2: x∙1=x
Truth Table
Theorem 2.ms14
Theorem 2 |  | 
x∙1=x |  | 
x | y | 
0 | 1 | 0
1 | 1 | 1
The theorem is proven by simulation.
If any variable is ANDed with 1, the result must be that variable.

## Slide 5: Theorem 3
Theorem 3: x∙x=x
Truth Table
Theorem 3.ms14
Theorem 3 |  | 
x∙x=x |  | 
x |  | 
0 | 0 | 
1 | 1 | 
The theorem is proven by simulation.
If any variable is ANDed with itself, the result is that variable.

## Slide 6: Theorem 4
Theorem 4: x·x̅=0
Truth Table
Theorem 4.ms14
Theorem 4 |  | 
x·x̅=0 |  | 
x |  | 
0 | 0 | 
1 | 0 | 
The theorem is proven by simulation.
If any variable is ANDed with the opposite of itself, the result is 0.

## Slide 7: Theorem 5
Theorem 5: x+0=x
Truth Table
Theorem 5.ms14
Theorem 5 |  | 
x+0=x |  | 
x | y | 
0 | 0 | 0
1 | 0 | 1
The theorem is proven by simulation.
If any variable is ORed with 0, the result is that variable.

## Slide 8: Theorem 6
Theorem 6: x+1=1
Truth Table
Theorem 6.ms14
Theorem 6 |  | 
x+1=1 |  | 
x | y | 
0 | 1 | 1
1 | 1 | 1
The theorem is proven by simulation.
If any variable is ORed 1, the result is always 1.

## Slide 9: Theorem 7
Theorem 7: x+x=x
Truth Table
Theorem 7.ms14
Theorem 7 | 
x+x=x | 
x | 
0 | 0
1 | 1
The theorem is proven by simulation.
If any variable is ORed with itself, the result is that variable.

## Slide 10: Theorem 8
Theorem 8: x+x̅=1
Truth Table
Theorem 8 | 
x+x̅=1 | 
x | 
0 | 1
1 | 1
Theorem 8.ms14
The theorem is proven by simulation.
If any variable is ORed with the opposite of itself, the result must be 1.

## Slide 11: Theorem 13a
Theorem 13a: x(y+z)=xy+xz
Truth Table
Theorem 13a |  |  | 
x(y+z)=xy+xz |  |  | 
x | y | z | 
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Theorem 13a.ms14
The theorem is proven by simulation.
Distributive law

## Slide 12: Theorem 13b
Theorem 13b: (w+x)(y+z)=wy+xy+wz+xz
Truth Table
Theorem 13b.ms14
Theorem 13b |  |  |  | 
(w+x)(y+z)=wy+xy+wz+xz |  |  |  | 
w | x | y | z | 
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
The theorem is proven by simulation.
Distributive law, part 2

## Slide 13: Theorem 14
Theorem 14: x+xy=x
Truth Table
Theorem 14.ms14
Theorem 14 |  | 
x+xy=x |  | 
x | y | 
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
The theorem is proven by simulation.
If any variable is ANDed with a second variable, and the result ORed with the first variable, the result is the first variable.

## Slide 14: Theorem 15a
Theorem 15a: x+x̅y=x+y
Truth Table
Theorem 15a.ms14
Theorem 15a |  | 
x+x̅y=x+y |  | 
x | y | 
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
The theorem is proven by simulation.
If the inverse of any variable is ANDed with another variable, and the result ORed with the first variable, the final result will be equal to the result from ORing the first variable with the second.

## Slide 15: Theorem 15b
Theorem 15b: x̅+xy=x̅+y
Truth Table
Theorem 15b.ms14
Theorem 15b |  | 
x̅+xy=x̅+y |  | 
x | y | 
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
The theorem is proven by simulation.
If any variable is ANDed with another variable and the result ORed with the first variable, the result is equal to ORing the inverse of the first variable with the second variable.

## Slide 16: Theorem 16
Theorem 16: (̅x̅+̅y̅)̅=x̅∙y̅
Truth Table
Theorem 16.ms14
Theorem 16 |  | 
(̅x̅+̅y̅)̅=x̅∙y̅ |  | 
x | y | 
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
The theorem is proven by simulation.
If any two variables are ORed together and the result NOTed, the result is equal to NOTing each variable individually and then ANDing the results.

## Slide 17: Theorem 17
Theorem 17: (̅x̅∙̅y̅)̅=x̅+y̅
Truth Table
Theorem 17.ms14
Theorem 17 |  | 
(̅x̅∙̅y̅)̅=x̅+y̅ |  | 
x | y | 
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
The theorem is proven by simulation.
If any two variables are ANDed and the result NOTed the result is equal to NOTing each variable individually and then ANDing them.