## Slide 1: Lab Notebook for EECT 121
Electronics Circuit Analysis
Nathaniel Paulus & Zachery Francis – Spring 2018

## Slide 2: Table of Contents
Lab 1 – Resistor Network Analysis
Review Lab 10 – Capacitors in Series and Parallel
Review Lab 11 – RC Lab
Review Lab 12 – Series/Parallel Inductors
Lab 3 – Diodes
Lab 4 – 9v Power Supply
BJTs
JFETs
Op-amps
Addendum: rectifiers

## Slide 3: Lab 1 – Resistor Network Analysis
Date: January 23, 2018
Lab partners: Nathaniel Paulus & Zachery Francis
Test equipment: N/A
Description: In this lab I used Multisim and Excel to analyze a resistor network (shown on the next page). I calculated voltage, current, power rating, voltage ranges given a part tolerance, and more.
Observations: Measurements are generally easier to do in Multisim (create the circuit, then measure the results). Calculations to determine how to build the circuit (e.g. how to modify circuit to create a given voltage) must be done mathematically, since Multisim doesn’t build a circuit given requirements, it only analyzes circuits the user builds.
Lab1.ms14
Lab 1.xlsx

## Slide 4: Lab 1 – Resistor Network Analysis
The circuit and instructions given for this lab.

## Slide 5: Lab 1 – Resistor Network Analysis
Part 1: The original circuit as described.

## Slide 6: Lab 1 – Resistor Network Analysis
Part 2: the circuit modified so that VA will be 2.5 times its original value.

## Slide 7: Lab 1 – Resistor Network Analysis
Part 4: Every resistor replaced with 1k.
(Part 3 does not have a simulation because it is calculating wattage needed for each resistor).

## Slide 8: Lab 1 – Resistor Network Analysis
Part 5: Measuring min and max VA given a 5% part tolerance, and measuring total resistance.

## Slide 9: Lab 1 – Resistor Network Analysis
All the Excel calculations for each step in this lab (vertical line divides each step). Best viewed directly in Excel: Lab 1.xlsx

## Slide 10: Review Lab 10 – Capacitors in Series and Parallel
Date: January 30, 2018
Lab partners: Nathaniel Paulus
Test equipment: GW Instek LCR-819
Description: In this lab I calculated how capacitors should combine in series and parallel. Then I measured it in the lab.
Observations: The first LCR meter I tried to use did not give reasonable values. The second one I tried (and ultimately used) gave more reasonable values, but they were always significantly below the expected values. The meter likely needs to be calibrated, though it’s also possible all the parts I used really were a good amount under their rating.
Review Lab 10.docx
Review Lab 10.xlsx
Review Lab 10.ms14

## Slide 11: Review Lab 10 – Capacitors in Series and Parallel
Calculating the total capacitance of the capacitors in series and parallel.

## Slide 12: Review Lab 10 – Capacitors in Series and Parallel
Measuring the total capacitance of the capacitors in series and parallel.

## Slide 13: Review Lab 11 – RC Lab
Date: April 3, 2018
Lab partners: Nathaniel Paulus
Test equipment: GW Instek LCR-819, GW Instek GDM-8245
Description: In this lab I created a RC (resistor &capacitor) circuit.
Observations: The LCR meter is either incredibly difficult to use, unreliable, or both. I usually have to try several of them before I find one that gives reasonable values.
Review Lab 11.docx
Review Lab 11.ms14

## Slide 14: Review Lab 11 – RC Lab
Each RC circuit with a different value capacitor.

## Slide 15: Review Lab 11 – RC Lab
Measured and expect values. This was after several tries to get a good reading from an LCR meter. The 1k resistor was surprisingly close to its nominal value.

## Slide 16: Review Lab 12 – Series/Parallel Inductors
Date: 2018-04-17
Lab partners: Nathaniel Paulus
Test equipment: GW Instek LCR-819
Description: In this lab I calculated, measured, and simulated the combined values of three inductors when they were alternately in series or parallel.
Observations: For each of the inductors I measured the measured value was greater than the nominal value. However, when I measured them in series the measured value was less than the sum of the values. This suggests that a significant part of the error is due to the meter, not the inductors it is measuring.
Lab 12.docx
Lab 12.xlsx
Lab 12.ms14

## Slide 17: Review Lab 12 – Series/Parallel Inductors
Series and parallel inductors in Multisim.

## Slide 18: Review Lab 12 – Series/Parallel Inductors
Calculating total inductance in series and parallel in Excel.

## Slide 19: Review Lab 12 – Series/Parallel Inductors
Measuring the inductors in series.

## Slide 20: Review Lab 12 – Series/Parallel Inductors
Measuring inductance in parallel. This is less than 5% more than the expected value.

## Slide 21: Lab 3 – Diodes
Date: February 27, 2018
Lab partners: Zachery Francis, Nathaniel Paulus
Test equipment: N/A
Description: This lab experiments with different ways of using diodes.
Observations:
Forward and reverse biased diodes.ms14
Diode as waveform clipper.ms14
LEDs.ms14
Zener diodes.ms14

## Slide 22: Lab 3 – Diodes
Forward and reverse biased diodes. Forward biased means current is flowing in the direction the diode allows current to flow easily. Reverse biased means the current flows in the direction the diode resists.

## Slide 23: Lab 3 – Diodes
Diodes as a waveform clipper. Top: the diodes each rectify a different half of the sine wave. Bottom: Real-life diodes are not ideal. There is a brief delay before the diode becomes reverse-biased (the downward spike), and a certain voltage that has to be reached before the current is allowed to freely flow (the gradual slope before the sharp rise).

## Slide 24: Lab 3 – Diodes
Powering LEDs. Top left: The LED is forward-biased. The 500Ω resistor limits current to c. 24mA (9V/500Ω=24mA). Top right: The 2.2k resistor leaves to little power to light the LED. Bottom: The 500Ω resistor allows sufficient current to flow, but the diode is reverse-biased, preventing most of the current from flowing, therefore the LED does not light.

## Slide 25: Lab 3 – Diodes
Zener diodes being used to limit voltage. Despite the large difference in voltage (13V v. 18V) both loads (1kΩ resistors) have approximately the same voltage applied (c. 12V). This is because the 1N4742A has a reverse-bias breakdown at c. 12V. If a larger voltage is applied the Zener diode pulls enough current to drop the voltage down to 12V.

## Slide 26: Lab 4 – 9v Power Supply
Date: May 1, 2018
Lab partners: Nathaniel Paulus, Zachery Francis
Test equipment: N/A
Description: In this lab we designed a +/- 9v power supply in Multisim, capable of providing up to 100mA.
Observations: Getting the voltage just right is tricky. Not all of it was theory; in the end some of it involved changing values, such as the turn ratio, until it worked properly.
Transformers.ms14
Power supply.ms14

## Slide 27: Lab 4 – 9v Power Supply
Transformers step up (or down) AC voltage a rate equal to the turn ratio.
Top: The turn ratio is 120 to 9, so 120V is transformed to 9V (RMS).
Center: 120/9 ≈13.33. Therefore a turn ratio of 13.333 also yields 9V.
Bottom: Transformers can also increase voltage (at the cost of reduced current). Here the 1:3 turn ratio converts 120V to 360V.

## Slide 28: Lab 4 – 9v Power Supply
The final power supply design. It provides +9v on the bottom, and -9v on the top, with a maximum load of 100mA on each. A switch on each side can turn the power supply on and off, and fuses will cut the power if the current exceeds the maximum allowed.

## Slide 29: Lab 4 – 9v Power Supply
These oscilloscope readings show the voltage before and after it passes through the regulator. On the left is the -9v supply, and on the right is the +9v supply. The 60hz ripple is due to the charging and discharging of the capacitors by the 60hz power source.

## Slide 30: BJTs
Date: May 8, 2018
Lab partners: Nathaniel Paulus, Zachery Francis
Test equipment: N/A
Description: In this lab we experiment with controlling LEDs with BJTs, and with amplifying a signal by a factor of 10.
Observations: The current flow direction is a little confusing. In an NPN transistor current flows from the collector to the emitter. In the PNP, current flows from the emitter to the collector.
LED control.ms14
10x gain.ms14

## Slide 31: BJTs
Controlling an LED using a transistor. This circuit is about as simple as it can get. The 10k resistor pulls the base to ground when the switch is open. When the switch is closed the base is pulled to high. The 220 ohm resistor protects the LED from excessive current.

## Slide 32: BJTs
Amplifying a 1kHz 5mVpk signal by a factor of 10. The AC voltage on the left provides the input signal, and the output is between VOUT and ground.

## Slide 33: BJTs
Here we have the signal both before and after amplification via the circuit on the previous slide. The top waveform is from before amplification, and the bottom waveform after amplification. We can see that the output has 10x the magnitude of the input because they are equal in height, and channel B is scaled to a factor 10x smaller than channel A (5mv/Div v. 50 mv/Div).

## Slide 34: Op-amps
Date: May 11, 2018
Lab partners: Zachery Francis, Nathaniel Paulus
Test equipment: N/A
Description: This lab experiments, in Multisim, with low-pass, high-pass, notch-pass, and band-pass filters.
Observations:
High pass filter.ms14
Low pass filter.ms14
Bandpass filter.ms14
Notch pass filter (needs alittle work).ms14

## Slide 35: Op-amps
This is a high-pass filter. It “passes” higher frequencies, while attenuating (suppressing) lower frequencies.

## Slide 36: Op-amps
Green is the input, red is the output of the high-pass filter.
Top: a 10Hz signal in, a smaller signal out.
Bottom: a 100Hz signal in, a larger signal out.
The higher-frequency signal has been amplified, while the lower frequency signal has been attenuated.

## Slide 37: Op-amps
This is a low-pass filter. It serves the opposite function from the high-pass filter: it passes low frequencies while attenuating high frequencies.

## Slide 38: Op-amps
Top: A high frequency (green, 100kHz) signal is input to the filter, which attenuates the signal.
Bottom: A low frequency (green, 10Hz) signal is input to the filter, which amplifies the signal.

## Slide 39: Op-amps
This is a band pass filter. It passes a range of frequencies, while attenuating frequencies outside that range. A band pass filter can be constructed by combining a high-pass and low-pass filter.

## Slide 40: Op-amps
A band pass filter consists of two filters, one to block high frequencies, the other to block low frequencies. The frequencies that neither blocks is the band that is allowed to pass.
High frequencies
Low frequencies
Blocks high frequencies
Blocks low frequencies
Band of frequencies allowed to pass
The cut-off point is not a straight line but rather a curve on both top and bottom (more like this curve than the rounded rectangles).

## Slide 41: Op-amps
This is [supposed to be] a notch filter. It passes every frequency except a range of frequencies.
Note: I suspect there is a grievous wiring error in this schematic (e.g. the fact that the output is tied to -12V? That would seem to be problematic). Additionally, testing across ranges from 1mHz to 1PHz failed to produce any noticeable changes in the output (again, the output being tied to -12V seems like a very conspicuous problem).

## Slide 42: Op-amps
Rough diagram of frequencies passed v. frequencies attenuated. A notch filter filters out all frequencies in a given range and passes those that are above or below that range.
Passed
Attenuated
(partially or completely blocked)
Passed
High frequency
Low frequency

## Slide 43: Addendum: rectifiers
Rectifiers take an AC current and output a pulsating current that is not exactly DC, but the polarity does not change (it is all positive or all negative). There are several types of rectifiers:
Half-wave: Using a single diode it is possible to rectify AC, but this leaves large gaps when the diode is reverse biased.
Full-wave: Using two or more diodes, AC can be rectified without leaving large gaps (as in oscilloscope reading above), though there will still be enormous dips in the voltage. This works because when one diode is reverse biased, the other is forward biased, and when the one is forward biased, the other is reverse biased.

## Slide 44: Doughnuts