## Slide 1: Lab Notebook for EECT 211
AC Circuit Analysis
Isaiah Knaperek & Nathaniel Paulus – Spring 2019

## Slide 2: Table of Contents
Lab 11, 11.1, 13, and 13.1
Elvis manual 4.4, 4.5, and 4.6
RC Time Constant
High pass, low pass, band pass, and notch filter
Resistor network
Fourier analysis
Butterworth filter
Transformers
Diodes
Toroids

## Slide 3: Lab 11, 11.1, 13, and 13.1
Date: February 4-18, 2019
Lab partners: Isaiah Knaperek & Nathaniel Paulus
Test equipment: NI Elvis 2+, GW Instek LCR-819
Description: In this lab we built and tested passive first-order high pass and low pass RC and RL filters.
Observations: The low pass RC filter and the high pass RL filter phase change reverse direction at higher frequencies (that is to say, they begin to head in one direction, then start to head back in the other direction). We’re not sure the exact reason for this, but it’s possible parasitic inductance and capacitance plays a significant role.

## Slide 4: Lab 11
Calculations and measurements for 0.47uF, 1uF, and 2.2uF low pass RC filters, in the frequency domain.

## Slide 5: Lab 11
Simulated bode plots for 0.47uF, 1uF, and 2.2uF low pass RC filters, in the frequency domain.

## Slide 6: Lab 11
Bode plots for 0.47uF, 1uF, and 2.2uF low pass RC filters.

## Slide 7: Lab 11.1
Calculations and measurements for 0.47uF, 1uF, and 2.2uF high pass RC filters, in the frequency domain.

## Slide 8: Lab 11.1
Simulated bode plots for 0.47uF, 1uF, and 2.2uF high pass RC filters, in the frequency domain.

## Slide 9: Lab 11.1
Bode plots for 0.47uF, 1uF, and 2.2uF high pass RC filters.

## Slide 10: Lab 13
Calculations and measurements for 1.0mH, 2.2mH, and 4.7mH high pass RL filters, in the frequency domain.

## Slide 11: Lab 13
Simulated bode plots for 1.0mH, 2.2mH, and 4.7mH high pass RL filters, in the frequency domain.

## Slide 12: Lab 13
Simulated bode plots for 1.0mH, 2.2mH, and 4.7mH high pass RL filters.

## Slide 13: Lab 13
Calculations and measurements for 1.0mH, 2.2mH, and 4.7mH low pass RL filters, in the frequency domain.

## Slide 14: Lab 13
Simulated bode plots for 1.0mH, 2.2mH, and 4.7mH low pass RL filters, in the frequency domain.

## Slide 15: Lab 13.1
Bode plots for 1.0mH, 2.2mH, and 4.7mH low pass RL filters.

## Slide 16: Elvis manual 4.4, 4.5, and 4.6
Date: February 25-March 4, 2019
Lab partners: Isaiah Knaperek & Nathaniel Paulus
Test equipment: NI Elvis 2+, GW Instek LCR-819
Description: In this lab we built active first-order high-pass and low-pass filters, and a second-order band-pass filter.
Observations: In some of our bode plots the phase shift jumps from being delayed 180° (-180° phase shift) to being 180° ahead of the input signal (+180° phase shift). This is because Elvis only shows phase shifts between +180° and -180°. The actual phase shift has not suddenly jumped 360° higher, it has just gone below -180° and wrapped around to the other side.

## Slide 17: Elvis manual 4.4
Simulated bode plot for first-order high-pass filter.

## Slide 18: Elvis manual 4.4
Bode plot for first-order high-pass filter.

## Slide 19: Elvis manual 4.4
First-order high-pass filter.

## Slide 20: Elvis manual 4.5
Simulated bode plot for first-order low-pass filter.

## Slide 21: Elvis manual 4.5
Bode plot for first-order low-pass filter.

## Slide 22: Elvis manual 4.5
First-order low-pass filter.

## Slide 23: Elvis manual 4.6
Bode plot for second-order band-pass filter.

## Slide 24: Elvis manual 4.6
Simulated bode plot for second-order band-pass filter.

## Slide 25: Elvis manual 4.6
Second-order band-pass filter.

## Slide 26: RC Time Constant
Date: February 18-27, 2019
Lab partners: Isaiah Knaperek & Nathaniel Paulus
Test equipment: NI Elvis 2+, GW Instek LCR-819
Description: In this lab we analyzed the voltage response of RC circuits using the RC time constant.
Observations: The RC time constant is found by multiplying resistance by capacitance to yield time. At first glance these units appear to have nothing to do with time, and getting time as a result of the multiplication does not seem to make sense. However, the definition of the Ohm is , and the definition of the Farad is . When these are multiplied, all the units cancel except seconds.

## Slide 27: RC Time Constant
Calculations for the voltage response over time using the RC time constant.
Given a supply voltage V and a time constant RC, the voltage across the capacitor at time t will be .

## Slide 28: RC Time Constant
Using Multisim’s multimeter to measure voltage response 95ms after the input voltage changes.

## Slide 29: RC Time Constant
Measuring voltage response using NI Elvis oscilloscope.

## Slide 30: High pass, low pass, band pass, and notch filter
Date: February 25-April 1, 2019
Lab partners: Isaiah Knaperek & Nathaniel Paulus
Test equipment: NI Elvis 2+, GW Instek LCR-819
Description: In this lab we built active second-order high-pass, low-pass, band-pass, and notch filters, using an LM741 op-amp.
Observations: We had a lot of issues with the notch filter. The gain tended to swing wildly where the notch was supposed to be. Replacing one of the ceramic capacitors with a Mylar capacitor greatly reduced the issue. This was after the ceramic capacitor had already been replaced with another ceramic capacitor of equal value, with no noticeable improvement.

## Slide 31: High pass filter
Calculations and simulated bode plot for high-pass filter.

## Slide 32: High pass filter
Bode plot for high-pass filter.

## Slide 33: High pass filter
High-pass filter.

## Slide 34: Low pass filter
Calculations and simulated bode plot for low-pass filter.

## Slide 35: Low pass filter
Bode plot for low-pass filter.

## Slide 36: Low pass filter
Low pass filter.

## Slide 37: Band pass filter
Calculations and simulated bode plot for band-pass filter.

## Slide 38: Band pass filter
Bode plot for band-pass filter.

## Slide 39: Band pass filter
Band-pass filter.

## Slide 40: Notch filter
Calculations and simulated bode plot for notch filter.

## Slide 41: Notch filter
Bode plot for notch filter.

## Slide 42: Notch filter
Notch filter.

## Slide 43: Resistor network
Date: March 4-April 15, 2019
Lab partners: Isaiah Knaperek & Nathaniel Paulus
Test equipment: NI Elvis 2+
Description: In this lab we analyzed and built a resistor network. We then replaced two resistors with one to create an equivalent total resistance.
Observations: There is no simple way to find a combination of standard-value resistors that will create an exact resistance. The only feasible method is to use a brute force algorithm to find the best combination.

## Slide 44: Resistor network
R1 = 470
R2 = 470
R3 = 1K
R4 = 1K
R5 = 470
R6 = 470
1.) Using Excel and Multisim determine RT
2.) Build and measure RT
3.) Design new circuit with same RT using
five standard resistor values.
The circuit and instructions we were given.

## Slide 45: Resistor network
Calculations and measurements before and after the circuit was changed.

## Slide 46: Resistor network
Measuring the total resistance of the original circuit.

## Slide 47: Fourier analysis
Date: March 25-April 1, 2019
Lab partners: Isaiah Knaperek & Nathaniel Paulus
Test equipment: N/A
Description: In this lab we used Multisim to perform a Fourier analysis on a waveform. We then used multiple Multisim voltage sources to add the harmonics and reconstruct the waveform.
Observations: When the input signal was subtracted from the replicated harmonics and DC signal, it showed that the main deviations were at the first harmonic (120Hz). The second most dominant signal was at a frequency of 794.3Hz. This is closest to the 7th harmonic (840Hz), so we think it is the addition of all the frequencies from the 7th harmonic and higher.

## Slide 48: Fourier analysis
Using Multisim to test the results of our Fourier analysis. The Fourier analysis determined the magnitude and phase of the signal’s harmonics and DC voltage. The circuit on the right adds the harmonics back together to reconstruct the original waveform.

## Slide 49: Fourier analysis
Left: The input signal and the signal generated by adding six harmonics and the DC component. The two signals are so close that they almost completely overlap. Right: the rectified sine wave subtracted from replicated harmonics and DC signal (showing how close they are to the original input signal). The dominant frequency is 120Hz.

## Slide 50: Fourier analysis
Left: Fourier analysis data from Multisim. Right: transient analysis data plotted from Multisim.

## Slide 51: Butterworth filter
Date: April 8-15, 2019
Lab partners: Isaiah Knaperek & Nathaniel Paulus
Test equipment: NI Elvis 2+
Description: In this lab we designed, built, and analyzed a second-order Butterworth filter with a 3dB point at 500Hz.
Observations: The signal analysis shows that at a 50% duty cycle the DC component of the input signal had a gain of -40dB, at a 25% duty cycle it had a gain of about 2dB, and at a 10% duty cycle it had a gain of about 6dB.

## Slide 52: Butterworth filter
Results of the Fourier transform of the output of our filter when a square wave is applied at 50%, 25%, or 10% duty cycle at 2kHz. A 94ms delay from startup was added to avoid the result being influence by the initial charge-up time for the capacitors.

## Slide 53: Butterworth filter
The design of our Butterworth filter.

## Slide 54: Butterworth filter
Fourier analysis of the output of the filter at 50%, 25%, and 10% duty cycle, respectively.

## Slide 55: Butterworth filter
Blue: Square wave input to our filter. Green: the output of the Butterworth filter.
Note that the input signal has a magnitude of about 5V, and the output signal has a magnitude of about 391mV.

## Slide 56: Butterworth filter
Our Butterworth filter implemented on the NI Elvis board.

## Slide 57: Transformers
Date: April 15, 2019
Lab partners: Isaiah Knaperek & Nathaniel Paulus
Test equipment: GW Instek GDM-8245, ECG DM-305A, Tektronix TDS 220
Description: In this lab we connected two transformers to mains power and measured the output voltage and frequency.
Observations: The output RMS voltage of the transformers was significantly higher than their rated output. This could be due to the quality of the transformers, and the lack of a load.

## Slide 58: Transformers
We input mains power to each of the transformers and then measured the output voltage and frequency using the handheld multimeter, bench-top multimeter, and the oscilloscope. We also measured the resistance of the transformers using the handheld and benchtop multimeters.

## Slide 59: Transformers
Several oscilloscope readings from the transformers. The values on the oscilloscope are scaled by a factor of 1/10.
Left: The 24V transformer as measured between the right and left coils.
Center: The 24V transformer, each signal measured between the center tap and the right or left coil.
Right: The 12.6V transformer, each signal measured between the center tap and the right or left coil.

## Slide 60: Diodes
Date: April 15, 2019
Lab partners: Isaiah Knaperek & Nathaniel Paulus
Test equipment: N/A
Description: In this lab we attempted to design a diode in PSpice.
Observations: It was difficult to find a datasheet that supplied all the values we needed in order to build the model in PSpice. We ended up using a second datasheet to provide some of the missing information, particularly regarding the reverse leakage.

## Slide 61: Diodes
This page configures the model’s forward voltage v. current characteristics. The green line is PSpice’s best fit to the data. The data was taken from the 1n4007 datasheet on ivytechengineering.com.

## Slide 62: Diodes
Junction capacitance was also based off the datasheet from ivytechengineering.com. We couldn’t figure out why Pspice didn’t actually fit the line to the data we supplied. No matter what values we entered the green line did not change.

## Slide 63: Diodes
For the reverse voltage characteristics we had to turn to another datasheet (linked above). It provided the data in terms of peak reverse voltage. Based on both datasheets we consulted, this was 50V, so converted the percentages to a voltage as we input the data. Once again we couldn’t get PSpice to actually fit the line to the data.

## Slide 64: Diodes
According to the datasheet the maximum repetitive reverse voltage is 50V. We didn’t find values for Iz and Zz.

## Slide 65: Diodes
This is the last page of the model editor, and we didn’t find values for this page. We also didn’t get to the point of looking for values for the “parameters” frame at the bottom of the screen. This was as far as we got in the PSpice model editor before moving on to other projects the next week.

## Slide 66: Toroids
Date: April 29, 2019
Lab partners: Isaiah Knaperek & Nathaniel Paulus
Test equipment: GW Instek GFG-8210, Tektronix TDS 220, GW Instek LCR-819
Description: In this lab we calculated the inductance and magnetic flux of four toroids with 10 windings each. Then we measured the inductance. Then we added another 10 windings on the opposite side of the toroid to create a one-to-one isolation transformer, and measured the output waveform when a 1MHz sine wave was applied to the primary winding.
Observations: When we input a 100kHz sine wave the voltage dropped from 1Vpp to 288mVpp. This seemed extremely excessive, leading us to increase the input frequency to 1MHz in order to increase the impedance, which resolved the issue.

## Slide 67: Toroids
Our calculations of magnetic flux for each of the toroids wound 10 times. The value for the permeability was taken from the video documenting how to do the calculations. In the second row we calculated the approximate length of wire needed to wrap the toroids 10 times. We then measured the inductance of each of the toroids and the relative error between the expected and measured value. We found that the smallest error was over 93%, meaning the real-life inductance was nearly twice that of the theoretical inductance.

## Slide 68: Toroids
Measuring the output waveform when we input a sine wave on the primary winding (results on next slide).

## Slide 69: Toroids
The top waveform in each of these shows the signal applied to the primary winding of the torioids. The bottom waveform shows the output waveform on the secondary winding. The measurement on the left shows what happened when the input signal was at 100kHz. The input voltage was pulled down to 288mV peak-to-peak. We then increased the frequency to 1MHz, shown for the T37 and T80 toroids in the next two readings.

## Slide 70: The End