## Slide 1
EECT111 Notes
Using MultiSim, Excel and hand calculations create a set of notes that show how to:
1.) Multiple resistors combine in series and parallel.
2.) By example calculate RT, IT, PT, and all the nodal voltages, branch currents and power
dissipation of a resistor network.
3.) By example calculate the Thevenin Resistance and Voltage of a resistor network.
4.) Multiple capacitors combine in series and parallel.
5.) Multiple inductors combine in series and parallel.
6.) Using a simple RC circuit determine the
a.) Time Constant
b.) Create a graph that shows the RC time constant as a function of time
b.) Determine XC at a fixed frequency
d.) Create a graph that shows how XC changes as a function of frequency
e.) Create a graph showing the Frequency response.

## Slide 2
EECT111 Notes
Using MultiSim, Excel and hand calculations create a set of notes that show how:
7.) Using a simple RL circuit determine the
a.) Time Constant
b.) Create a graph that shows the RL time constant as a function of time
b.) Determine XL at a fixed frequency
d.) Create a graph that shows how XL changes as a function of frequency
e.) Create a graph showing the Frequency response.

## Slide 3
EECT111 Notes - Resistors
1.) How do multiple resistors combine in series and parallel?
Series
Parallel – 3 or more unequal resistors
Parallel – multiple equal value resistors
Parallel – two unequal value resistors
R1 = | 10000 |  | 
R2 = | 2200 |  | 
R3 = | 4700 |  | 
Rt = | 16900 | → | B3+B2+B1
R1 = | 1000 |  | 
R2 = | 1000 |  | 
R3 = | 1000 |  | 
R4 = | 1000 |  | 
Rt = | 250 | → | B12/4
R1 = | 4700 |  | 
R2 = | 1000 |  | 
Rt = | 824.5614 | → | (B19*B20)/(B19+B20)

## Slide 4
V1 = | 9 | Ω |  | 
R1 = | 470 | Ω |  | 
R2 = | 470 | Ω |  | 
R3 = | 1000 | Ω |  | 
R4 = | 1000 | Ω |  | 
R5 = | 2200 | Ω |  | 
R6 = | 3300 | Ω |  | 
R7 = | 4700 | Ω |  | 
R8 = | 10000 | Ω |  | 
R3&4 = | 500 | Ω |  | 
R5,6,7 = | 1030.565 | Ω |  | 
R345678 = | 11530.56 | Ω |  | 
R2345678 = | 451.5925 | Ω |  | 
RT = | 921.5925 | Ω |  | 
VA = | 4.410119 | V |  | 
VB = | 4.218883 | V |  | 
VC = | 3.824721 | V |  | 
IT = | 0.009766 | A | 9.765704 | mA
IR1 = | 0.009766 | A | 9.765704 | mA
IR2 = | 0.009383 | A | 9.383232 | mA
IR3 = | 0.000191 | A | 191.236 | uA
IR4 = | 0.000191 | A | 191.236 | uA
IR5 = | 0.000179 | A | 179.1647 | uA
IR6 = | 0.000119 | A | 119.4431 | uA
IR7 = | 8.39E-05 | A | 83.86431 | uA
IR8 = | 0.000382 | A | 382.4721 | uA
I check 1 | 0.000382 | ok | 382.4721 | uA
I check 2 | 0.000382 | FALSE | 382.4721 | uA
I check 3 | 0.009766 | ok | 9.765704 | mA
R3&4 = | =1/((1/B5)+(1/B4)) | 
R5,6,7 = | =1/((1/B6)+(1/B7)+(1/B8)) | 
R345678 = | =B10+B11+B9 | 
R2345678 = | =1/((1/B3)+(1/B12)) | 
RT = | =B13+B2 | 
VA = | =B1*B13/B14 | 
VB = | =B15-(B10*B26) | 
VC = | =B16-((B11)*B26) | 
IT = | =(B1/B14) | =B18*1000
IR1 = | =(B1/B14) | =B19*1000
IR2 = | =B15/B3 | =B20*1000
IR3 = | =B26/2 | =B21*1000000
IR4 = | =B26/2 | =B22*1000000
IR5 = | =(B16-B17)/B6 | =B23*1000000
IR6 = | =(B16-B17)/B7 | =B24*1000000
IR7 = | =(B16-B17)/B8 | =B25*1000000
IR8 = | =B15/B12 | =B26*1000000
I check 1 | =B21+B22 | =B27*1000000
I check 2 | =B23+B24+B25 | =B28*1000000
I check 3 | =B26+B20 | =B29*1000
2.) By example calculate RT, IT, PT, and all the nodal voltages, branch currents and power
dissipation of a resistor network.
EECT111 Notes - Resistors

## Slide 5
EECT111 Notes
3.) By example calculate the Thevenin Resistance and Voltage of a resistor network.
Vin = | 9 | V
R1 = | 1000 | Ω
R2 = | 4700 | Ω
R3 = | 4700 | Ω
R4 = | 2200 | Ω
R5 = | 3300 | Ω
R6 = | 4700 | Ω
R23 = | 9400 | Ω
R123 = | 903.8462 | Ω
R45 = | 1320 | Ω
R12345 = | 2223.846 | Ω
Rth = | 1509.577 | Ω
Vth = | 6.109321 | V
Vin = | 9
R1 = | 1000
R2 = | 4700
R3 = | 4700
R4 = | 2200
R5 = | 3300
R6 = | 4700
R23 = | =B3+B4
R123 = | =(B2*B8)/(B2+B8)
R45 = | =(B5*B6)/(B5+B6)
R12345 = | =B9+B10
Rth = | =(B11*B7)/(B11+B7)
Vth = | =(B1*B7)/(B7+B11)

## Slide 6
EECT111 Notes
4.) Multiple capacitors combine in series and parallel.
Circuit 1
Series
Circuit 1
Parallel
Calculations 

## Slide 7
Reciprocal approach | 
C1 = | 1.0E-6
C2 = | 470.0E-9
C3 = | 100.0E-9
Ct = | 76.2E-9
Equal Value approach | 
C1 = | 1.0E-6
C2 = | 470.0E-9
Ct = | 500.0E-9
Product over sum approach | 
C1 = | 470.0E-9
C2 = | 470.0E-9
Ct = | 235.0E-9
Reciprocal approach | 
C1 = | 470.0E-9
C2 = | 470.0E-9
Ct = | 235.0E-9
Parallel | 
C1 = | 1.0E-6
C2 = | 470.0E-9
C3 = | 100.0E-9
Ct = | 1.57E-06
Series | 
Xc = | 2.1E+3
freq = | 1000
C = | 76.2E-9
Reciprocal approach |  |  | Reciprocal approach | 
C1 = | 0.000001 |  | C1 = | 0.00000047
C2 = | 0.00000047 |  | C2 = | 0.00000047
C3 = | 0.0000001 |  | Ct = | =1/((1/E3)+(1/E2))
Ct = | =1/((1/B3)+(1/B2)+(1/B4)) |  |  | 
 |  |  | Parallel | 
Equal Value approach |  |  | C1 = | 0.000001
C1 = | 0.000001 |  | C2 = | 0.00000047
C2 = | 0.00000047 |  | C3 = | 0.0000001
Ct = | =B8/2 |  | Ct = | =SUM(E7,E8,E9)
Product over sum approach |  |  | Series | 
C1 = | 0.00000047 |  | Xc = | =1/(2*PI()*E14*B5)
C2 = | 0.00000047 |  | freq = | 1000
Ct = | =B13*B14/(B13+B14) |  | C = | =1/(2*PI()*E14*E13)
Capacitor Series/Parallel calculations

## Slide 8
EECT111 Notes
5.) Multiple inductors combine in series and parallel.
Inductors in series |  |  | 
L1 = | 0.1 | H | 
L2 = | 0.05 | H | 
L3 = | 0.2 | H | 
Lt = | 0.35 | H | B2+B3+B4
Inductors in parallel |  |  |  |  | 
L1 = | 0.1 | H |  |  | 
L2 = | 0.05 | H |  |  | 
L3 = | 0.2 | H |  |  | 
Lt = | 0.0286 | H | 1/((1/B8)+(1/B9)+(1/B10)) |  | 

## Slide 9
EECT111 Notes
6.) Using a simple RC circuit determine the
a.) Time Constant
b.) Create a graph that shows the RC time constant as a function of time
b.) Determine XC at a fixed frequency
d.) Create a graph that shows how XC changes as a function of frequency
e.) Create a graph showing the Frequency response.

## Slide 10
EECT111 Notes
6.) Using a simple RC circuit determine the
a.) Time Constant
V = | 1 | V | 
R = | 1000 | Ω | 
C1 = | 1.0E-6 |  | 
C2 = | 470.0E-9 |  | 
C3 = | 100.0E-9 |  | 
Xc = | 1.57E-06 | → | B5+B4+B3
Vc = | 0.63 | V | 
T = | 1.57E-03 | → | B6*B2

## Slide 11
6.) Using a simple RC circuit determine the
b.) Create a graph that shows the RC time constant as a function of time

## Slide 12
EECT111 Notes
6.) Using a simple RC circuit determine the
c.) Determine Xc at a fixed frequency
Freq = | 1000 |  |  | 
C1 = | 1.00E-06 |  |  | 
C2 = | 4.70E-07 |  | Formulas | 
C3 = | 1.00E-07 |  |  | 
C = | 1.57E-06 | Parallel | B2+B3+B4 | 
Xc= | 1.01E+02 |  | 1/(2*PI()*B1*B5) | 

## Slide 13
EECT111 Notes
6.) Using a simple RC circuit determine the
d.) Create a graph that shows how Xc changes as a function of frequency
Lab
Results

## Slide 14
6.) Using a simple RC circuit determine the
e.) Create a graph showing the Frequency response.

## Slide 15
1 | 1 | 1 | 0 |  | freq | Vin | Va |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10 | 1 | 1 | 0 |  | 10 | 1 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
20 | 1 | 0.984 | -0.140098031 |  | 20 | 1 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
30 | 1 | 0.968 | -0.282492854 |  | 30 | 1 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
40 | 1 | 0.936 | -0.574483025 |  | 40 | 1 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
50 | 1 | 0.904 | -0.87663139 |  | 50 | 1 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
60 | 1 | 0.864 | -1.26972515 |  | 60 | 1 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
70 | 1 | 0.824 | -1.681455766 |  | 70 | 1 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
80 | 1 | 0.784 | -2.113678746 |  | 80 | 1 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
90 | 1 | 0.752 | -2.475643188 |  | 90 | 1 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
100 | 1 | 0.712 | -2.950400127 |  | 100 | 1 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
110 | 1 | 0.688 | -3.248231235 |  | 1000 | 1 | 0.9 | -0.91515 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
120 | 1 | 0.656 | -3.661923212 |  | 2000 | 1 | 0.76 | -2.38373 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
130 | 1 | 0.624 | -4.096308206 |  | 3000 | 1 | 0.6 | -4.43697 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
140 | 1 | 0.592 | -4.553565866 |  | 4000 | 1 | 0.5 | -6.0206 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
150 | 1 | 0.56 | -5.03623946 |  | 5000 | 1 | 0.44 | -7.13095 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
160 | 1 | 0.544 | -5.288022006 |  | 6000 | 1 | 0.38 | -8.40433 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
170 | 1 | 0.512 | -5.81460078 |  | 7000 | 1 | 0.34 | -9.37042 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
175 | 1 | 0.504 | -5.951389271 |  | 8000 | 1 | 0.3 | -10.4576 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
177 | 1 | 0.5 | -6.020599913 |  | 9000 | 1 | 0.28 | -11.0568 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
180 | 1 | 0.496 | -6.09036647 |  | 10000 | 1 | 0.26 | -11.7005 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
190 | 1 | 0.48 | -6.375175252 |  | 20000 | 1 | 0.18 | -14.8945 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
200 | 1 | 0.464 | -6.669640389 |  | 30000 | 1 | 0.14 | -17.0774 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
300 | 1 | 0.328 | -9.682523126 |  | 40000 | 1 | 0.14 | -17.0774 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
400 | 1 | 0.256 | -11.83520069 |  | 50000 | 1 | 0.12 | -18.4164 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
500 | 1 | 0.208 | -13.6387333 |  | 60000 | 1 | 0.12 | -18.4164 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
600 | 1 | 0.176 | -15.08974664 |  | 70000 | 1 | 0.12 | -18.4164 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
700 | 1 | 0.16 | -15.91760035 |  | 80000 | 1 | 0.12 | -18.4164 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
800 | 1 | 0.144 | -16.83275016 |  | 90000 | 1 | 0.1 | -20 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
900 | 1 | 0.128 | -17.85580061 |  | 100000 | 1 | 0.1 | -20 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1000 | 1 | 0.112 | -19.01563955 |  | 1000000 | 1 | 0.1 | -20 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2000 | 1 | 0.064 | -23.87640052 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3000 | 1 | 0.048 | -26.37517525 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4000 | 1 | 0.032 | -29.89700043 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5000 | 1 | 0.032 | -29.89700043 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10000 | 1 | 0.016 | -35.91760035 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Chart: 
| 1 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 175 | 177 | 180 | 190 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 2000 | 3000 | 4000 | 5000 | 10000
 | 1 | 1 | 0.984 | 0.968 | 0.936 | 0.904 | 0.864 | 0.824 | 0.784 | 0.752 | 0.712 | 0.688 | 0.656 | 0.624 | 0.592 | 0.56 | 0.544 | 0.512 | 0.504 | 0.5 | 0.496 | 0.48 | 0.464 | 0.328 | 0.256 | 0.208 | 0.176 | 0.16 | 0.144 | 0.128 | 0.112 | 0.064 | 0.048 | 0.032 | 0.032 | 0.016
Chart: 
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 20000 | 30000 | 40000 | 50000 | 60000 | 70000 | 80000 | 90000 | 100000 | 1000000
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.9 | 0.76 | 0.6 | 0.5 | 0.44 | 0.38 | 0.34 | 0.3 | 0.28 | 0.26 | 0.18 | 0.14 | 0.14 | 0.12 | 0.12 | 0.12 | 0.12 | 0.1 | 0.1 | 0.1
Chart: 
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | -0.91515 | -2.3837 | -4.437 | -6.0206 | -7.1309 | -8.4043 | -9.3704 | -10.4576 | -11.0568 | -11.7005 | -14.8945 | -17.0774 | -17.0774 | -18.4164 | -18.4164 | -18.4164 | -18.4164 | -20 | -20 | -20
Chart: 
 | 0 | 0 | -0.1401 | -0.28249 | -0.57448 | -0.87663 | -1.2697 | -1.6815 | -2.1137 | -2.4756 | -2.9504 | -3.2482 | -3.6619 | -4.0963 | -4.5536 | -5.0362 | -5.288 | -5.8146 | -5.9514 | -6.0206 | -6.0904 | -6.3752 | -6.6696 | -9.6825 | -11.8352 | -13.6387 | -15.0897 | -15.9176 | -16.8328 | -17.8558 | -19.0156 | -23.8764 | -26.3752 | -29.897 | -29.897 | -35.9176

## Slide 16
EECT111 Notes
7.) Using a simple RL circuit determine the
a.) Time Constant
b.) Create a graph that shows the RL time constant as a function of time
c.) Determine XL at a fixed frequency
d.) Create a graph that shows how XL changes as a function of frequency
e.) Create a graph showing the Frequency response.

## Slide 17
EECT111 Notes
7.) Using a simple RL circuit determine the
a.) Time Constant

## Slide 18
EECT111 Notes
7.) Using a simple RL circuit determine the
b.) Create a graph that shows the RL time constant as a function of time.

## Slide 19
EECT111 Notes
7.) Using a simple RL circuit determine the
c.) Determine XL at a fixed frequency

## Slide 20
EECT111 Notes
7.) Using a simple RL circuit determine the
d.) Create a graph that shows how XL changes as a function of frequency
Xl = | 2*pi*F*L | 
L = | 1.00E-03 | H
 | Freq | xl
 | 0 | 0.00E+00
 | 10 | 6.28E-02
 | 20 | 1.26E-01
 | 30 | 1.88E-01
 | 40 | 2.51E-01
 | 50 | 3.14E-01
 | 60 | 3.77E-01
 | 70 | 4.40E-01
 | 80 | 5.03E-01
 | 90 | 5.65E-01
 | 100 | 6.28E-01
 | 1000 | 6.28E+00
 | 2000 | 1.26E+01
 | 3000 | 1.88E+01
 | 4000 | 2.51E+01
 | 5000 | 3.14E+01
 | 6000 | 3.77E+01
 | 7000 | 4.40E+01
 | 8000 | 5.03E+01
 | 9000 | 5.65E+01
 | 10000 | 6.28E+01
 | 20000 | 1.26E+02
 | 30000 | 1.88E+02
 | 40000 | 2.51E+02
 | 50000 | 3.14E+02
 | 60000 | 3.77E+02
 | 70000 | 4.40E+02
 | 80000 | 5.03E+02
 | 90000 | 5.65E+02
 | 100000 | 6.28E+02
Chart: Frequency
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 20000 | 30000 | 40000 | 50000 | 60000 | 70000 | 80000 | 90000 | 100000
 | 0 | 0.062832 | 0.12566 | 0.1885 | 0.25133 | 0.31416 | 0.37699 | 0.43982 | 0.50265 | 0.56549 | 0.62832 | 6.2832 | 12.5664 | 18.8496 | 25.1327 | 31.4159 | 37.6991 | 43.9823 | 50.2655 | 56.5487 | 62.8319 | 125.6637 | 188.4956 | 251.3274 | 314.1593 | 376.9911 | 439.823 | 502.6548 | 565.4867 | 628.3185

## Slide 21
7.) Using a simple RL circuit determine the
e.) Create a graph showing the Frequency response.