## Slide 1
Introduction to Circuits Analysis
by Andrew G. Bell
abell118@ivytech.edu
(260) 481-2288
Lecture 11

## Slide 2: CHAPTER 11
Basic AC Quantities

## Slide 3: AC and DC Differences
Alternating Current
Current: Magnitude and direction change periodically
Voltage: Magnitude and direction change periodically
Sine Wave: Most common representation

## Slide 4: AC and DC Differences (cont.)
Direct Current
Current: Single magnitude and direction
Voltage: Single magnitude and direction

## Slide 5: AC Power and Transmission
AC advantageous over DC in transmission of power over long distances
AC has ability to be stepped up or down
AC easily produced by generators

## Slide 6: AC and DC Characteristics

## Slide 7: Mathematical Concepts
360° angular motion
0° starting point
Angles increase in positive CCW direction
Maximum positive value at 90°
0 volts at 180°
Maximum negative value at 270°

## Slide 8: Generating AC Voltage
Voltage developed by wire moving in magnetic field

## Slide 9: Radians and Degrees
Radians Degrees
0 0°
/2 90°
 180°
3/2 270°
2 360°

## Slide 10
Use Excel create a plot of the Sine and Cosine functions
Remember, Excel uses radians not degrees so all angles must be converted to radians
Excel

## Slide 11: Flux Lines and Induced Voltage
Zero volts at 0°,180°, and 360°
Maximum at 90° and 270°
Positive values between 0° and 180°
Negative values between 180° and 360°

## Slide 12: Sine Wave Summary
Amplitude characteristics follow sine function.
Amplitude constantly varies in value.
Direction periodically reverses.

## Slide 13: Sine Wave Terms
Cycle: 360°
Period (T): Time required to complete a cycle
  Unit of Measure: Seconds (sec)
Frequency (f): Number of cycles in a second
  Unit of Measure: Hertz (Hz)
Alternation: Half of a sine wave

## Slide 14: Equations

## Slide 15: Commercial Power
Period = 16.67 milliseconds
Frequency = 60 Hertz

## Slide 16: Phase Relationships

## Slide 17: Phase Relationships (cont.)
In Phase: When two voltages or currents have the same frequency and pass through zero and reach their maximums at the same time
Out of Phase: When two voltages or currents are the same frequency but pass through zero and reach their maximums at different times

## Slide 18: AC Measurements
Peak: Ip or Vp
Peak-to-Peak: 2 × Vp
Average: 0.637 × Vp
Effective: rms value, 0.707 × Vp
Instantaneous: v = Vp sin 

## Slide 19: Purely Resistive Circuit

## Slide 20: Other Periodic Waveforms
Square wave
Rectangular wave
Sawtooth wave

## Slide 21: Parameters
Pulse Width: Time a waveform is positive-going
Period: Time between positive-going transitions
Duty Cycle: Pulse width divided by the period