## Slide 1
Introduction to Circuits Analysis
by Andrew G. Bell
abell118@ivytech.edu
(260) 481-2288
Chapter 17
Capacitance

## Slide 2: Capacitor
An electrical component consisting of two conductors (plates) separated by an insulator (dielectric)
A component that opposes a change in circuit voltage

## Slide 3: Dielectric Materials
Vacuum Glass
Air Ceramic
Paper Aluminum Oxide
Plastic Tantalum Oxide

## Slide 4: Electrical Definition of Capacitor
An electrical component that stores energy in the form of electrical charge when voltage is applied

## Slide 5: Basic Symbols

## Slide 6: Capacitor Action
Applied voltage forces electrons onto one plate. The electrostatic field associated with a charged particle forces electrons off of the opposite plate.

## Slide 7: Capacitor Charging
Applied voltage causes circuit current to flow. Plates of the capacitor become charged as one plate accumulates electrons and the other releases electrons. Circuit action continues until:
VC = VS

## Slide 8: Capacitor Discharge
A charged capacitor will discharge when a path is provided between the two plates.
The plate with excess electrons will give up electrons to the plate with a deficiency until:
VC = 0 V

## Slide 9: The Farad
Capacitance is the capacity of a capacitor to store electrical charge.
The unit of measure is the farad (f).

## Slide 10: Charge and Voltage

## Slide 11: Energy Stored in Field
Energy = joules stored
C = capacitance (farads)
V = voltage

## Slide 12: Factors and Value
ITEM
Plate area
Plate distance
Dielectric material
RELATIONSHIP
Direct
Inverse
Direct

## Slide 13: Dielectric Constant
0: Absolute permittivity of dielectric
materials
v: Absolute permittivity of vacuum

## Slide 14: Dielectric Types

## Slide 15: Dielectric Strength
The breakdown voltage rating of a given material and dimensions
Dielectric material reaches point where punch-through occurs

## Slide 16: Capacitor Formula
C = capacitance (farads)
A = area of plates (sq. meters)
s = spacing between plates (meters)
8.85 = constant for air/vacuum
Use Excel to evaluate how Area, Spacing and dielectric constant change the capacitance of a parallel plate capacitor
Excel

## Slide 17: Finding Total Capacitance
For series capacitors:
  Sum of the reciprocals

## Slide 18: Finding Total Capacitance (cont.)
For two series capacitors:
  Product-over-the-sum

## Slide 19: Finding Total Capacitance (cont.)
For parallel capacitors:
  Direct summation

## Slide 20: Total Capacitance
Using Excel calculate the total capacitance of each circuit
Excel

## Slide 21: Series Voltage Distribution
VX = voltage across capacitor x
VS = DC source voltage
CT = total series capacitance
CX = value of capacitor x

## Slide 22: Example
Multisim
Use Multisim determine the voltage across each capacitor
Multisim

## Slide 23: Charge Distribution
In parallel circuits:

## Slide 24: RC Time Constant ()
Time required for a capacitor to charge or discharge 63.2% of the change in voltage level applied
Five time constants are needed to fully charge/discharge

## Slide 25: Time Constant Chart

## Slide 26
Assuming a 9V Square wave input Use Multisim and Excel to determine the RC Time Constant and plot the transient response
Multisim
Excel
R = | 1.0E+3 | ohms
C = | 47.0E-6 | farad
t = | 47.0E-3 | seconds
5t = | 235.0E-3 | seconds
pulse width = | 235.0E-3 | seconds
period = | 470.0E-3 | seconds

## Slide 27: Exponential Form for Charging Capacitors
 = epsilon (or 2.71828)
t = time allowed (seconds)
 = R × C (or 1 time constant)

## Slide 28: Exponential Form for Discharging Capacitors
 = epsilon (or 2.71828)
t = time allowed (seconds)
 = R × C (or 1 time constant)

## Slide 29: Capacitor Types
FIXED
Paper/Plastic
Mica
Ceramic
Electrolytic
Chip
VARIABLE
Trimmer
Air

## Slide 30: Ratings
Temperature
Tolerance
Voltage Rating
Temperature Coefficient
Power Factor
Inductance Characteristics (at high frequencies)

## Slide 31: Safety
Always discharge circuit capacitors after power has been removed and before working on circuits containing them.
Observe polarity when connecting electrolytic capacitors into a circuit.

## Slide 32: Ratings
Physical Size and Mounting
Capacitance Value
Capacitance Tolerance
Working Voltage Ratings
Temperature Range
Temperature Coefficient
Inductance

## Slide 33: Typical Problems
Ohmmeter Tests
Opens
Shorts