## Slide 1: Lab 5 NPN Transistor Switch
By: Dakota Johnson
Lab Partner: Josiah Abel
Instructor: Andy Bell
Bench Number: 6
Class: EECT 121-50C
Date: 12/15/2015

## Slide 2: Objectives:
To turn on an LED with an NPN transistor.
Equipment and Parts:
    GW Instek LCR meter model#: LCR-819 SN#: E120998
    DC Power Supply Model# HY1802D
    Digital Multi Meter Brand: GwInstek Model #: GDM-8245 SN: CL860332
    LM317 Voltage Regulator
    74LS04 Hex Inverter
    2N2222 NPN Transistor
    LED
    220Ω Resistor
    6.8KΩ Resistor
    270Ω Resistor
    10kΩ potentiometer

## Slide 3: Data/Lab Results/Simulations/Schematics:
Multisim Schematics of the circuit.
Simulation of the circuit with the LED off.
Simulation of the circuit with the LED on.

## Slide 4
Component | Measured | Expected | 
Resistor | 26.9E+3 | 27.0E+3 | Ω
Resistor | 216 | 220 | Ω
Resistor | 326.87 | 330 | Ω
Potentiometer | 640 | N/A | Ω
Circuit with LED off
Circuit with LED on
Voltage readings of 9V and 5V sources.
LM317 Voltage Regulator
220Ω Resistor
10kΩ Potentiometer
270Ω Resistor
LED
2N2222 NPN Transistor
74LS04 Hex Inverter
6.8kΩ Resistor

## Slide 5: Troubleshooting:
  The switch for the inverter was left floating. Once the switch was properly grounded the circuit worked as planned.

## Slide 6: Conclusion:
A transistor can be used as a switch

## Slide 7: Data Sheets:
74LS04 Hex Inverter
2N2222 NPN Transistor
LM317 Voltage Regulator