## Slide 1: Lab 7 N-Type JFET Switch
By: Dakota Johnson
Lab Partner: Josiah Abel
Instructor: Andy Bell
Bench Number: 6
Class: EECT 121-50C
Date: 12/15/2015

## Slide 2: Objectives:
To turn on an LED with an N-Type JFET transistor.
Equipment and Parts:
    DC Power Supply Model# HY1802D
    Digital Multi Meter Brand: GwInstek Model #: GDM-8245 SN: CL860332
    LED
    4.7kΩ Resistor
    2N5457 N-Type JFET Transistor

## Slide 3: Data/Lab Results/Simulations/Schematics:
.model 2N5457DHJ NJF(Vto=-1.372 Beta=1.125m Lambda=2.3m
+ Vtotc=-2.5m Is=181.3f Isr=1.747p N=1 Nr=2 Xti=3 Alpha=2.543u
+ Vk=152.2 Cgd=4p M=.3114 Pb=.5 Fc=.5 Cgs=4.627p Kf=10.45E-18
+ Betatce=-.5 Rd=1 Rs=1 Af=1)
Model of 2N5457 used in the simulations
Type | Current |  | Voltage Drop | 
08LX330 HV12 | 1.354 | mA | 3.582 | V
08L803 | 2.792 | mA | 1.945 | V
08L1043 | 3.049 | mA | 1.688 | V
08L93SRC | 2.999 | mA | 1.738 | V
08L32 | 2.818 | mA | 1.934 | V
08LX330 HV5 | 2.34 | mA | 2.491 | V
08LX330 HV5 | 2.844 | mA | 1.905 | V
08l53 | 2.899 | mA | 1.843 | V
Multisim Schematics of the circuit.
Simulation of the circuit with the LED on.
Simulation of the circuit with the LED off.
Table of LEDs measured in lab

## Slide 4
LED
2N5457 N-Type JFET Transistor
4.7kΩ Resistor
Circuit with LED off
Circuit with LED on

## Slide 5: Troubleshooting:
  The LED in the simulation was not functioning properly. It was found that the transistor could not generate a current strong enough to turn on the LED. To solve this, LEDs from the lab were measured and the current threshold of the LED on the simulation was changed to the measured currents for the LEDs. Once this was done the circuit worked properly.

## Slide 6: Conclusion:
JFET transistors can be used as a voltage controlled switch.

## Slide 7: Data Sheets:
2N5457 N-Type Transistor