## Slide 1: Lab 10
By: Dakota Johnson
Lab Partner: Josiah Abel
Instructor: Andy Bell
Bench Number: 6
Class: EECT 122-20C
Date: 3/18/2015

## Slide 2: Objectives:
To build a MOD-12 counter circuit and test the total propagation delay of the circuit.
Equipment and Parts:
Equipment | Model/Part Number | Serial Number
NI Elvis II+ | 19857OA-02L | 1677D1E
Digital Multimeter | GW INSTEK GDM-8245 | CL860332
Tektronix TDs 220 2-Channel Ocilloscope | TDS220 | B083266
Function Generator | GW INSTEK GFG -8210 | C705245
Part | Amount
330 Resistors | 4
74LS08D Chip | 1
74LS112D Chip | 2
74LS04D Chip | 1
74LS00D Chip | 1
LED 08LX330HV5 | 4
Miscellaneous Wires | ------------

## Slide 3: Data/Lab Results/Simulations/Schematics:
0001
0010
0011
0100
0000
1011
1111
1101
1110
1100
1010
1001
1000
0111
0110
0101
Temporary State
State Transition Diagram

## Slide 4
74LS04
74LS00
74LS08
74LS112
330 Resistors
Output Voltages |  | 
 | High Voltage | Low Voltage
 | (V) | (V)
MSB | 3.84 | 0.1
3rd Bit | 3.84 | 0.113
2nd Bit | 3.84 | 0.109
LSB | 3.85 | 0.113
Total Propagation Delay
Time
(ns)
20
Clock Frequency
Frequency
(kHz)
1.08

## Slide 5: Troubleshooting:
  One major problem was that the counter would count to 12 instead of 11.
    The problem was found to be in the initial design. The original schematic was for a MOD-13 not a MOD-12. The schematic was rebuilt and simulated and the changes were implemented into the physical design. Once this was done the problem was resolved.

## Slide 6: Conclusion:
The Circuit was successfully built and the total propagation delay was found to be 20ns.

## Slide 7: Data Sheets:
74LS08
74LS112
74LS04
74LS00