## Slide 1: EECT 112 LAB NOTEBOOK
Josiah Abel
Fall 2014
Instructor: Louis Toth
Partner/Assistant: Dakota Johnson

## Slide 2: TABLE OF CONTENTS
LAB # | LAB TITLE | SLIDE LOCATION
LAB 1 | AND, OR Gates | (3-12)
LAB 2 | Alternative NAND | (13-25)
LAB 3 | Car Alarm (Midterm) | (26-33)
LAB 4 | Binary Counter | (34-42)
LAB 5 | Basic Stamp 1LED Flasher | (43-48)
LAB 6 | Basic Stamp 2 Temp Sensor/Heater | (49-56)

## Slide 3: LAB 1: AND, OR Gates

## Slide 4
Equipment:
Breadboard – NIELVIS II+ , SN: 14C6E29
Digital Multimeter(DMM) – GWINSTEK GDM-3245, SN: CL860334
AND Gate – chip number: 74LS08D
OR Gate – chip number: 74LS32D
Miscellaneous Wiring
Objective:
To Demonstrate and become familiar with wiring a digital circuit, specifically one using an AND gate or an OR gate.

## Slide 5
AND GATE AND TRUTH TABLE:
AND GATE:
A and B represent the inputs to the gate. In an AND gate, ALL of the inputs must have a logic of 1 to trigger a high for the whole gate.
TRUTH TABLE:
A truth table demonstrates what the output of a system will be for every possible input combination.
1 = Logic True, 0 = Logic False

## Slide 6: OR Gate and Truth Table:
OR GATE:
A and B represent the inputs to the gate. In an OR gate, only one of the inputs must have a logic of 1 to trigger a high for the whole gate.
TRUTH TABLE:
A truth table demonstrates what the output of a system will be for every possible input combination.
1 = Logic True, 0 = Logic False

## Slide 7: PROCEDURE:
A Multisim 13.0 schematic was constructed
Circuits were built in the lab to confirm operation of AND & OR gates using Elvis II+ proto boards.
Information to hook up the chips was found online and the datasheets were recorded
Also took pictures of the circuit when LED is ON and OFF

## Slide 8
LAYOUT / SETUP OF BREADBOARD:
AND gate
OR gate
Resistors
Input A
Input B

## Slide 9: PINOUTS FOR AND/OR GATES:
A Pinout is a diagram which displays each pin’s function on a logic chip
GROUND
POWER
POWER
AND GATE
OR GATE

## Slide 10: RESULT LEDS on:
AND GATE
OR GATE
RESISTORS
LEDS
AND switch
OR switch

## Slide 11: RESULT LED OFF:
AND GATE
OR GATE
RESISTORS
LEDS
AND switch
OR switch

## Slide 12: CONCLUSION:
After the circuits for both AND & OR gates had been wired they were tested and found to be true to the Multisim 13.0 Schematic.

## Slide 13: LAB # 2: ALTERNATE nand

## Slide 14
Equipment:
Breadboard – NIELVIS II+ , SN: 1677D1E
Digital Multimeter (DMM) – GWINSTEK GDM-8245, SN: CL860332
AND Gate – chip number: 74LS08D
OR Gate – chip number: 74LS32D
NOT Gate – chip number: 74LS04D
NAND Gate – chip number: 74LS00D
Miscellaneous Wiring
Objective:
T0 simplify a digital circuit by using less chips and by using the Boolean operation of inverting both inputs and outputs to change the gates function.

## Slide 15
AND GATE AND TRUTH TABLE:
AND GATE:
A and B represent the inputs to the gate. In an AND gate, ALL of the inputs must have a logic of 1 to trigger a high for the whole gate.
TRUTH TABLE:
A truth table demonstrates what the output of a system will be for every possible input combination.
1 = Logic True, 0 = Logic False

## Slide 16
NOT GATE AND TRUTH TABLE:
NOT GATE:
A represents the input to the gate. In an NOT gate, ALL of the inputs That have a logic of 1 have an output of 0. ALL inputs that have an input of 0 have an output of 1. This gate is also called an inverter.
TRUTH TABLE:
A truth table demonstrates what the output of a system will be for every possible input combination.
1 = Logic True, 0 = Logic False

## Slide 17: NAND Gate and Truth Table:
NAND GATE:
A and B represent the inputs to the gate. In an NAND gate, both of the inputs must have a logic of 0 to trigger a high for the whole gate. Because the NAND function inverts the inputs.
TRUTH TABLE:
A truth table demonstrates what the output of a system will be for every possible input combination.
1 = Logic True, 0 = Logic False

## Slide 18: OR Gate and Truth Table:
OR GATE:
A and B represent the inputs to the gate. In an OR gate, only one of the inputs must have a logic of 1 to trigger a high for the whole gate.
TRUTH TABLE:
A truth table demonstrates what the output of a system will be for every possible input combination.
1 = Logic True, 0 = Logic False

## Slide 19
GROUND
POWER
NOT GATE
NAND GATE
NAND, NOT PINOUTS:
NOT CHIP
NAND CHIP

## Slide 20
MULTISIM 13.0 SCHEMATIC:
OR GATE
NAND GATE
NOT GATE
INPUT SWITCHES
AND GATE

## Slide 21: PROCEDURE:
Constructed a Circuit containing NOT, OR, & AND Gates creating it so that the inputs to two OR gates were inverted then their outputs were wired into the inputs of an AND gate. This assembly was wired to an LED On the Proto Board.
Another circuit was constructed with the same output using just NAND gates.
Voltage of the circuit was measured when LEDs were On.
Voltage Was measured when the LEDs were off.
Voltage was measured when the LEDs were disconnected from the circuit.

## Slide 22
INPUT SWITCHES
NAND GATES
NOT GATE
AND GATE
OR GATE
RESISTORS
LED INPUTS

## Slide 23: LED ON and Off:
LED ON
LED OFF

## Slide 24: Digital Multi meter voltage measurements:
LED ON
VOLT: 3.1784
LED OFF
VOLT: 0.1000
LED DISCONNECTED
VOLT: 4.3927

## Slide 25: CONCLUSION:
By using the property of inverting inputs and outputs of a gate, it reverses the gate’s function. (AND becomes OR)
This principle may be used to reduce the number of chips utilized within a circuit.
When the voltage measurements were taken the difference between when the LED was off and on is explained by the fact that the power is being routed through all the components for LED on and it is being routed to ground for LED off.
When the LEDs were removed the voltage reading was higher because it had less resistance traveling through the circuits.

## Slide 26: LAB # 3:CAR ALARM (Midterm)

## Slide 27
Equipment:
Multisim 13.0 computer program
Breadboard – NIELVIS II+ , SN: 1677D1E
2 AND Gates – chip number 74ls08D
2 OR Gates – chip number 74ls32D
1 NOT Gate – chip number 74ls04D
3 10k Resistors
Assorted Wiring
OBJECTIVE:
To design the logic for a "Black Box“ of unknown circuitry. To use the given input and output requirements and recreate this circuit from start to finish.

## Slide 28: PROCEDURE:
DESCRIPTION
the stated requirements concerned a car alarm. there are three input variables, the car's driver's side front door, the headlights and the ignition, all of which were set to active low meaning that they gave a logic of 1 when a switch toggled to ground. when the door was opened and either the lights or the ignition are on, a gentle beeping car alarm will sound to indicate to the driver that they must close the door before driving or shut the lights or ignition off before getting out of the vehicle. the same alarm will trigger if the ignition is turned off while the headlights remain on.

## Slide 29: PROCEDURE Continued:
First A truth table was created.
The Boolean Algebra expression was found and simplified
Multisim 13.0 computer program was used to construct a working virtual circuit.
Then the circuit was built and demonstrated in the lab.

## Slide 30: Diagram of project:
The Goal was to create a simplified circuit that would fulfill the necessary requirements to trigger the alarm.

## Slide 31: Truth Table
INPUT DOOR (D) | INPUT HEADLIGHTS (L) | INPUT IGNITION (I) | OUTPUT ALARM
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
1 = Logic True, 0 = Logic False = Not
The Boolean equation derived from the table is: (L)(I)(D)+(D)(I)(L)+(D)(I)(L)+(D)(I)(L)
Using DeMorgen’s Theorems, the expression can Be simplified to the equation: (I)(D) + L(I)

## Slide 32
MULTISIM 13.0 DIAGRAM:
AND Gates
NOT Gate
Activator switches
L = lights, D = door
I = ignition
OR Gate

## Slide 33: CONCLUSION:
The Circuitry designed fulfilled the requirements for the Car Alarm outlined in the Procedure. By following the Procedure from start to finish an ideal logic circuit could be created.
When the door was opened while the lights or ignition were engaged the LED lit up to signal that the alarm was sounding.
When the ignition was turned off while the headlights were on the LED lit up again to indicate that the alarm was sounding.

## Slide 34: LAB # 4: Binary counter

## Slide 35
EQUIPMENT:
NI ELVIS II+ , SN: 1677D3B
Function Generator computer program, NI_ELVISmx
Tektronix TDS 220, Two channel, (Digital real-time Oscilloscope), SN: B068379
4-Bit Ripple Counter chip – 74ls93P
BCD To 7 Segment Decoder chip – 74ls48P
Man 74 – 7 segment display
1 10k resistor
Assorted wiring
OBJECTIVE: To Use NI Elvis II+ to build 4-bit binary counter with hex 7-segment display that counts from zero to F in the Hexadecimal system (0-15).

## Slide 36: PROCEDURE:
Multisim 13.0 was utilized to create a Working schematic
Digital clock
Man 74, 7 seg. display
RESET

## Slide 37: PROCEDURE Continued:
The pinout for the Man 74 7 segment display was researched so that the proper output wires from the Decoder could be inserted to create the proper number on the display for the current count.
Example: by applying power to a, b, c, d, e and f the number 0 would appear on the display.
Example: by applying power to a, b, and c the number 7 would appear on the display.

## Slide 38: PINOUTS, Counter and decoder:
Clock INPUTS
Output Power to 7-Segment Display
Count Variable Outputs
GROUND
POWER
Counter Inputs
COUNTER CHIP
DECODER CHIP

## Slide 39: Setup:
7 – SEGMENT
DISPLAY
COUNTER
CHIP
DECODER
CHIP
FUNCTION GENERATOR COMPUTER PROGRAM
The Function Generator was plugged into the Proto board to create a Clock that the Counter Chip could interpret.

## Slide 40: Physical representation:
The Clock created by the function generator program was given a physical display using the Tektronix TDS 220, Two channel, (Digital real-time Oscilloscope). This way when the clock was changed to a faster or slower period the Clock could be observed over channel 1.
OBSERVABLE
COUNT

## Slide 41: RESULT AFTER wiring:
RECOGNIZABLE NUMBERS:
-0
-1
-3
-4
-5
-7
-8
-9

## Slide 42: CONCLUSION:
By Using The new 4-Bit Ripple Counter chip and the BCD To 7 Segment Decoder chip it was possible to construct a Counting circuit with a 7-segment display
The Count in Multisim 13.0 was programmable, therefore you could modify exactly how each number in the count was displayed. When it was physically represented on the Proto Board the numbers displayed skipped around because of mismatched programing between the Decoder and the Counter chips.

## Slide 43: lab # 5: Basic Stamp 1 Led flasher

## Slide 44
EQUIPMENT:
Industrial Control Student Workbook Version 1.1
One red LED
2 220 ohm resistors
1 10k ohm resistor
1 dipswitch (wire)
BASICSTAMP II device
BASICSTAMP program
Miscellaneous Wiring
OBJECTIVE:
To Program and build a simple circuit using the BASICSTAMP computer program and by wiring a BASICSTAMP II board.

## Slide 45: PROCEDURE:
In the Industrial Control Student Workbook Version 1.1, Experiment #1, Exercise #2, LED Blinking Circuit, a simple circuit was laid out that contained a single LED output and Pushbutton input. A program was designed for when the pushbutton is pressed, the LED would flash 5 times over a 10 second interval, then stop and wait for another press of the pushbutton.
In the BASICSTAMP Programing process, commands had to be researched to determine exactly what the Program should tell the BASICSTAMP II board.

## Slide 46: BASICSTAMP II BOARD SETUP:
Resistors
Output Pin
Input Pin
Pushbutton

## Slide 47: Blinking led PROGRAM FILE:
KEY:
Green Text = Comments, A description of each line of code
Blue Text = Commands, A specified word for the BASICSTAMP program to perform a certain function.
Black Text = Titles of variables and routines in the program.
Define variables
Define Pins
Initial Conditions
INITIAL LOOP
BLINK LED LOOP
Go back to 1st loop

## Slide 48: BLINKING LED RESULT:
In The short video clip, it is demonstrated that the LED will blink like it was programed to do.
CONCLUSION: Plainly stated,
BASICSTAMP IS AWESOME!!
Also by using the simple commands of BASICSTAMP a simple PLD it is possible to create a working circuit which responds to various Inputs and functions.

## Slide 49: Lab # 6: Basic stamp 2 temp sensor/heater

## Slide 50
EQUIPMENT:
Industrial Control Student Workbook Version 1.1
BASICSTAMP II device
BASICSTAMP program
1 10K Potentiometer (Variable Resistor), VR
1 uF Capacitor
1 red LED
2 22o ohm resistors
1 10k ohm resistor
Small flat – headed screwdriver(to adjust variable resistor)
Assorted Wiring
OBJECTIVE:
TO Combine the understanding of a digital program and outputs with that of an ANALOG input and to use the DEBUG process to display the effects.

## Slide 51: PROCEDURE:
In the Industrial Control Student Workbook Version 1.1, instructions for Experiment #1, Exercise #3, Analog Data Input, were located.
A program was Composed to simulate the process of a Heater Control, using an RC network with a capacitor and potentiometer.
The temperature was represented by the Potentiometer (Variable Resistor) and could be increased or decreased using a small flat-headed screwdriver to precisely turn the variable screw on top of the resistor. This “heat” was monitored and the heater was energized (RED LED ON) below 100 degrees and de-energized (RED LED OFF) above 120 degrees. The Debug window was used to display the temperature and status of the heater.

## Slide 52: Basicstamp II board setup:
Input Pin
Output Pin
Capacitor
Variable Resistor

## Slide 53: Temp sensor/heater Program:
KEY:
Green Text = Comments, A description of each line of code
Blue Text = Commands, A specified word for the BASICSTAMP program to perform a certain function.
Black Text = Titles of variables and routines in the program.
Red Text = Debug command.
Define variables
Define Pins
And Initial Conditions
MAIN LOOP
READ VR
Initialize DEBUG
IF VR is Low enough
Turn ON heater
Go Back to MAIN LOOP
IF VR HIGH enough
Turn OFF heater

## Slide 54: RESULTS, HEATER ENERGIZED:
HEATER
(Energized)
POTENTIAOMETER (VR)
LEFT: BASICSTAMP while running the program and while the heater was ON.
BELOW: DEBUG screen feedback located on the computer screen. It displays the point and temperature at which the heater was energized.

## Slide 55: RESULTS, HEATER DE-ENERGIZED:
HEATER
(DE-Energized)
POTENTIAOMETER (VR)
LEFT: BASICSTAMP while running the program and while the heater was OFF.
BELOW: DEBUG screen feedback located on the computer screen. It displays the point and temperature at which the heater was DE-Energized.

## Slide 56: CONCLUSION:
By adding the Variable resistor, The result of the program could be determined entirely from the analog change of the Resistor.
The DEBUG sequence makes it possible for differentiating between analog inputs (VR) and digital outputs (LED).