## Slide 1: Lab Notebook
Brandon Steup EECT-111

## Slide 2: Lab 0
Though more of a proof on concept, lab 0 had us measuring resistors and comparing them to what they in theory should be.
In the measurements, they proved that the resistors will always be off from what they are rated to be due to tolerenceing during when they are being made.

## Slide 3: Lab 0 Excel
Resisters | Actual Measured | Theoretical | Difference | Tolerence
1K Resister | 981.0E-3 | 1.0E+0 | 18.7E-3 | -0.02%
First 10K | 9.8E+0 | 10.0E+0 | 230.0E-3 | -0.02%
Second 10K | 9.8E+0 | 10.0E+0 | 245.0E-3 | -2.50%
 | 20.5E+0 |  |  | 
Total | 20.5E+0 | 21.0E+0 | 493.7E-3 | -2.40%

## Slide 4: Lab 1 (Brandon Steup and Corey King)
Lab 1 involved taking a sample of 20 1k resistors and measuring each one to see what the parts actual resistivity was, then comparing that to the 5% deviance that is supposed to be allowed.
In all of the samples that we took, none of them went out of that 5% spec.
This lab did not involve any simulation, hence the lack of multisim photos.

## Slide 5: Lab 1 Procedure
Select a set of 20 resistors with the same color code and thus the same value
Measure each of them using the multimeter and record the resistance
Enter all of them into a chart so that we can observe the varience in each of the resistors.

## Slide 6: Lab 1 Table of Resistor Values
 | Resistance KΩ
1 | 0.999
2 | 0.9997
3 | 0.9887
4 | 1.0046
5 | 1.0035
6 | 0.9872
7 | 0.9929
8 | 0.9914
9 | 0.9889
10 | 1.0018
11 | 1.0004
12 | 1.0016
13 | 1.0004
14 | 0.998
15 | 1.0023
16 | 1.0007
17 | 0.9989
18 | 0.9994
19 | 0.9849
20 | 1.002
Minimum KΩ | Maximum KΩ | Average KΩ | Standard Deviation KΩ
0.9849 | 1.0046 | 0.997315 | 0.005977614

## Slide 7: Lab 1 Observations
This lab mainly served to prove what I already know, that parts like this always will be off from what the spec says that are going to be.
This is due to defects or inconstancy's in the manufacturing process.
Another observation was that using the default method of measuring them was a pain, and I should have used alligator clips
Along with this, the answer to the final question in the lab was if any of the parts exceeded the 5% tolerance, and none of them did, however some of them came pretty close.

## Slide 8: Lab 2 (Brandon Steup and Corey King)
Lab 2 didn’t involve any simulation, it just involved taking measurements of resistors of varying values.
The main idea of this lab being understanding how the color codes worked and giving us a base for understanding what value a resistor was from the code.

## Slide 9: Lab 2 Procedure
Take 15 different resistors of varying values.
Figure out what value each of them are using the color code present on the resistor
Sort them from smallest to largest by resistance
Record data and observations.

## Slide 10: Lab 2 Observations
Given that the only thing to lab 2 was the understanding of how to read the color codes on the resistors, it was pretty dry.
In the table to the left, we can see the same type of deviation that we saw in lab 1, however here we can see that the deviation does scale with the resistance that the resistor is rated to have.

## Slide 11: Lab 3 (Brandon Steup and Corey King)
Lab 3 was the start of us working with measuring and creating in the lab circuits consisting of resistors wired in parallel.
The results that we recorded were consistent with the math worked out in excel, as well as being consistent with what we observed in the simulation.
The calculated voltage drops were consistent with what we calculated in excel using the resistors measured values.

## Slide 12: Lab 3 Pictures

## Slide 13: Lab 3 Multisim and Excel
Part 1 |  |  | 
Resistor | Measured | Calculated | Simulated
R1 | 10.0E+3 | 10.0E+3 | 10.0E+3
R2 | 2.2E+3 | 2.2E+3 | 2.2E+3
R3 | 4.6E+3 | 4.7E+3 | 4.7E+3
RT | 16.9E+3 | 16.9E+3 | 16.9E+3
Part 2 |  |  | 
 | Measured | Calculated | Simulated
It | 5.019E-04 | 532.0E-6 | 532.0E-6
V1 | 8.97 | 9 | 9
VA | 3.64 | 3.67 | 3.67
VB | 2.49 | 2.5 | 2.5

## Slide 14: Lab 3 Observations
One of the major issues that I kept having is that I would get backwards if the rows or columns were wired together.
Another interesting thing is in going through the data, seeing the error in the resistors propagate through the rest of the data, and how it throws everything a little bit off.

## Slide 15: Lab 4
We were required to create a circuit that fit the qualifications that used a 9 volt DC source and had an amperage of 10 mA
The circuit itself was pretty simple, consisting of 3 different resistors, 100 ohms, 330 ohms, and 470 ohms
As far as observations go, It was pretty useful the different ways that you could use ohms law to calculate the resistance values in excel by simply going through the available resistors.

## Slide 16: Lab 4 Excel and Multisim
 | Design |  | Measured |  | Calculated |  | Simulated | 
V1 = | 9 | v | 9 | v | 9 | v | 9 | v
IT = | 0.01 | A | 0.01018 | A | 0.01 | A | 0.01 | A
RT = | 900 | W | 884.05 | W | 900 | W | 900 | W
R1 = | 100 | W | 98.3 | W | 100 | W | 100 | W
R2 = | 470 | W | 462.35 | W | 330 | W | 330 | W
R3 = | 330 | W | 323.4 | W | 470 | W | 470 | W
R test = | 900 | W |  |  |  |  |  | 

## Slide 17: Lab 4 Observations
One of the major things that I learned from this lab was how to use excel and use the equation functions to make the calculations more efficient and also modular to a certain extent, making trying different values incredibly easy.

## Slide 18: Lab 5 (Brandon Steup and Corey King)
Lab 5 was pretty different from all of the other labs that we had done because it involved us using graphite mixed with a binder to draw a circuit on the cut off top of a balloon stretched over the top of a paint can. The purpose was to draw a circuit that made a MEMs variable resistor that the value of the total resistance would change when force was applied to it.
This lab had several issues arise, not least of which was the drawn circuit itself and the inconstant application of the graphite slurry in drawing the circuit.

## Slide 19: Lab 5 measurements
These measurements were taken at each point that we had copper tape in the loop then a total resistance value was also taken.
These measurements are far from approximate, they are messy, and due to the flaky nature of the setup, the results were very flakey and even absent at some points.

## Slide 20: Lab 5 Observations
This lab, was to say the least very weird. Setting up the lab, grinding up the graphite, and trying to paint a circuit was very odd to me, I understood the principles but the execution to me just felt odd.
As far as the circuit goes, it was only a half success, we were able to collect some data, and go through the lab, but the data we got was very flakey, the values kept changing with no interaction, and kept getting weaker until we got nothing at all.
However, we were able to observe the rise and fall of the resistance by pressing on the balloon, it just was vert inconstant.

## Slide 21: Lab 6 (Brandon Steup and Corey King)
Lab 6 was very similar to Lab 4, we had to create a circuit that fit the specifications that were given to us. The task was to design a circuit that used a 9 volt source, parallel resistors, and had a measure current draw of 18mA
The circuit that fulfilled these requirements used two 1000 ohm resistors to get a total resistance of 500, then using ohms law to confirm that the current drawn was indeed 18mA, which it was.

## Slide 22: Lab 6 Excel and Multisim
 | Design |  | Measured |  | Calculated |  | Simulated | 
V1 = | 9 | v | 9 | v | 9 | v | 9 | v
IT = | 0.018 | A | 0.018352 | A | 0.018 | A | 0.018 | v
RT = | 500 | W | 490.4147 | W | 500 | W | 500 | W
R1 = | 1000 | W | 985.35 | W | 1000 | W | 1000 | W
R2 = | 1000 | W | 976.35 | W | 1000 | W | 1000 | W
R test = | 500 | W |  |  |  |  |  | 

## Slide 23: Lab 6 Observations
I was blown away that to solve this circuit, it required 2 1000 ohm resistors, I thought it was going to be more complicated then that.
I realized that after running all of the numbers, I should have realized that through using ohms law and my usual calculations, it made perfect sense.
One of my big takeaways was how to go about thinking about the problem, we can only build with certain resistors, which narrows it down, and using multisim and running the calculations, just replacing the resistors till its correct works well and pretty efficiently. Especially considering excel is not my strongest suit.

## Slide 24: Lab 7 (Brandon Steup)
Lab 7 involved us creating, measuring, simulating, and testing a 4 resistor parallel circuit. This purpose of this was to teach and familiarize working with a more complex variant of a type of circuit that we had been previously introduced to.
The voltage used was 9 volts
All of the resistors that were used in this circuit were wired up in parallel
Resistor values were 2.2K, 3.3k, and two 4.7k’s

## Slide 25: Lab 7 Excel
R1= | 2200 | Ω |  | 
R2= | 3300 | Ω |  | 
R3= | 4700 | Ω |  | 
R4= | 4700 | Ω |  | 
RT= | 845.2316 | Ω |  | 
Vt= | 9 | V |  | 
I1= | 4.091E-3 |  |  | 4.090909
I2= | 2.727E-3 |  |  | 2.727273
I3= | 1.915E-3 |  |  | 1.914894
I4= | 1.915E-3 |  |  | 1.914894
It= | 10.648E-3 |  |  | 10.64797

## Slide 26: Lab 7 Multisim

## Slide 27: Lab 7 Pictures

## Slide 28: Lab 7 Observations
As far as observations go, the only thing that I really have to say is that when you get more then a few components in a single circuit it makes troubleshooting any mistakes that might have been made in wiring it more difficult to diagnose.
With that being said, it was also a lot more fun, it gave more interesting readings in the form of the branch currents, and also allowed us to use more of the equipment on the bench
Last observation would be the difficulty in setting up the measuring equipment, most of if not all of the mistakes that I made were related to setting up the test equipment.

## Slide 29: Lab 8 (Brandon Steup)
Lab 3 was one of the more interesting labs in my personal opinion. The goal of this lab was through the use of 3 resistors of the same value in a black box, to create a circuit that produced an output voltage of 1.3V
After we created that circuit however, the secondary requirement was then to take the first resistor, and change it in the simulation so we get exactly 1.3 volts, unlike the first result which was only close to 1.3V

## Slide 30: Lab 8 Multisim and Excel
 | Design | Measured | 
R1= | 4700 | 4610 | 
R2= | 4700 | 4689 | 
R3= | 4700 | 4591 | 
R4= | 4700 | 4622 | 
R5= | 4700 | 4626 | 
R(Black Box)= | 1566.66667 | 1537 | 
R1adj= | 4580 | 4580 | 
 | Measured | Calculated | Simulated
V1= | 9 | 9 | 9
VA= | 5.164 | 5.14 | 5.14
VB= | 3.8743 | 3.86 | 3.86
VA-VB= | 1.2893 | 1.28 | 1.28
(VA-VB)adj= | 1.3 | 1.3 | 1.3

## Slide 31: Lab 8 Observations
Lab 8 was particularly odd for me because again it was 3 4.7k resistors that gave us the value we needed, not because the math was weird, its just that seems to be the past labs the pattern for the black boxes, just a pattern I noticed.
Data wise I thought it was pretty interesting how tuning the R1 by just a little bit, we could dial in the voltage pretty easy.

## Slide 32: Lab 10 (Brandon Steup Corey Townsend)
The purpose of this lab was to delve into creating capacitor circuits, and learn how they combine and also how to measure things in a new unit type, called the farad.
They types of circuits that we made in this lab was one parallel and one series, both of them using 10, 22, and 47 micro farad capacitors.
The measurements were taken using an LCR meter on the bench and we also did a simulation in multisim and did the calculations for what it should have been in excel, as well as crunched the recorded data.

## Slide 33: Lab 10 Pictures

## Slide 34: Lab 10 Excel and Multisim

## Slide 35: Lab 10 Observations
The set up was very similar to our early labs for measuring resistance in resistor circuits, with the main difference being that we used different measuring equipment.
Data wise not many surprises, they were about the same as what we calculated them to be, plus or minus a little bit as per we have some to expect.
I did notice that when you touch the capacitors after them being tested, I did notice a tingling, not data related just something that I thought was interesting.

## Slide 36: Lab 11 (Brandon Steup and Corey Townsend)
The purpose of lab 11 was to construct 3 different circuits using the same parts except for one, that one being a different capacitor for each circuit, them being 0.47, 1, and 2.2 micro farad.
Then using these circuits, we were to sweep through them using an oscilloscope, which gave us the change between our input and output voltage as a function of the frequency.

## Slide 37: Lab 11 Measurements

## Slide 38: Lab 11 Multisim

## Slide 39: Lab 11 Observations
The use of the oscilloscope was something that was completely new to me, and was something that took some hooking up and about 2 hours of messing with.
Also adjusting and dialing in the frequency was something that was very touchy, and did vary a little bit, as well as even the oscilloscope had some variance between each one.
As far as the data goes, it was pretty close to what we calculated, once we got the multisim working. Overall this was one of the harder labs in the semester.

## Slide 40: Lab 12 (Brandon and Justin)
The purpose of this lab was to construct and measure circuits that include inductors, however the method for measuring the inductors was very similar to the last lab.
We used the LCR meter to measure the values of the inductors before we started building the circuits, as well as used it to take the value of the circuits themselves.
We introduced a new unit, the Henry
This also tied in with lab 13 in the same way that Lab 11 did with Lab 10.

## Slide 41: Lab 12 Measurements
 | Series | Parallel
I1 | 1 | 1
I2 | 2.2 | 2.2
I3 | 4.7 | 4.7
It | 7.9 | 599.8E-3

## Slide 42: Lab 12 Multisim

## Slide 43: Lab 12 Observations
One of the major things that I noticed, whether it was a result of getting better parts with more consistent readings, out data was more consistent then the past labs.
I was also using a different bench and thus different equipment, and that seems to be a factor in the above.
As far as gathering the data and the data itself, aside from the above it was very similar to the last two labs, just measuring a different component in a similar mannor.

## Slide 44: Lab 13 (Brandon Justin)
Lab 13 was the inductor version of Lab 11, however with more measurements taken.
We were to, again, create 3 different circuits using inductors of values of 1, 2.2, and 4.7.
Same as before, we put the circuit together in multisim, and then used the AC sweep to calculate every needed value in the table
Then we used the oscilloscope to measure several different points per circuit, and as planned they were pretty consistent.

## Slide 45: Lab 13 Multisim

## Slide 46: Lab 13 Excel

## Slide 47: Lab 13 Observations
This lab was one of the most in-depth labs to date, and the data and information supports that.
We calculated the values all of the of the frequencies for all three circuits in an ideal world, but only measured ten of the frequencies for each circuit.
Noticed that the inductors were very stable data wise, dialing everything in once we got the scope set up was much faster, and the numbers had less jitter then the capacitors.
Also with the multisim, the wiring having to include some resistor for both this lab and the last was something that I thought was crazy, and took me a while of playing with until you told me.

## Slide 48: Thank you for the amazing semester!
I hope you have an amazing summer 